## Slide 1: Upgrade to the Target Controller’s ROM Tables
P J Smith
21st March 2012

## Slide 2: The Controller ROM Table
The controller’s ROM table maps the target position to coil switching. (i.e. at position ‘x’ switch ‘on’ phases A -> B’)
This table has 3 columns, one for accelerating the target up, one for accelerating the target down and a final one for levitating the target.
Note that although the target controller has a positional resolution of 0.15mm, the coil switching has a resolution of 3mm. (This is the pitch of the coils.)
Currently only 2 phases out of the target’s 3 phases are powered at any time.
I have had the idea for some time that for various positions we could map the coils to switch all 3 coil phases on simultaneously, this should give several advantages.

## Slide 3: Updated ROM Tables
I’ve reprogrammed the ROM tables to include some additional states where all 3 phases are on simultaneously. These additional states improves the coil switching resolution from 3.0mm to 1.5mm.
Expected Advantages:
Improves switching resolution:
- more accurate capture => reduced settling time.
- Keeps the max force closer to its peak value; this improves the target’s efficiency (this should be a couple of % effect) .
Reduces the resistance of the coil stack to ~0.75R when all three phases are on:
- Higher current at a given voltage -> increases net force. (1.33 x I but 3 phases only on 50% of time & additional switching/resistive/inductive losses => so expect <16% net increase in force.)
Expected Disadvantages:
Stator will run slightly warmer.
May see more overshoots/undershoots due to improved capture resolution.

## Slide 4: Tests
Testing has so far been VERY limited, as I’ve had to take readings manually using the terminal application. I need to get the GUI updated so that I can get (much) more data… Both new and old ROM tables are in memory and can be switched on demand.
(ROM 1 = original, ROM 2 = new) Running at 0.5 Hz

## Slide 5: Tests
Taking fractional change = 0.95:
So (hopefully) we should be seeing a change in the acceleration of approximately 10% !!! I will try to confirm this when we have the GUI updated.

## Slide 6: Additional…
This is of no operational consequence whatsoever but…
It use to take about 30 seconds to move from park -> hold or back. This time period was a consequence of allowing the oscillations between each step (3.0mm) to dampen before moving the target to the next step.
Reduced step size of 1.5mm means significantly reduced oscillation between each step.
The lab target can now move from park -> hold (or vice versa) in ~4 seconds
(Quite impressive improvement when you’ve been watching it step so slowly for about 6 years!)